## Slide 1: HERCULES 2019 Simulating beamline optics by ray-tracing using ShadowOui
Manuel Sánchez del Río
AAM, ISDD, ESRF
2019 March 27th

## Slide 2: Goals Calculate main characteristics of synchrotron sources (dipoles and IDs) Simulating beamline optics by ray-tracing to obtain main parameters of beam size, energy resolution and flux Understand basic principles of x-ray optics: Reflective (aberrations, slope errors), Diffractive (dispersion) and Refractive (chromatic aberrations) A few words (only) about coherence

## Slide 3: The OASYS Project
OASYS = OrAnge SYnchrotron Suite
A common platform to build synchrotron-oriented User Interfaces that communicate
The upper layer of the application presented to the user
Open Source & Python technology
Luca Rebuffi
Manuel Sanchez del Rio
Luca Rebuffi, Manuel Sanchez del Rio (2017)
OASYS (OrAnge SYnchrotron Suite) : an open-source graphical environment for x-ray virtual experiments
Proc.SPIE 10388: 10388-10388. http://dx.doi.org/10.1117/12.2274263
https://oasys-kit.github.io/
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 4: Synchrotron Virtual Experiments
Storage Ring
(e- optics)
Radiation devices
(e- -> g)
Beamline
(g optics)
Sample
(g -matter interactions)
Beamline Experiment Chain
Shadow
WOFRY
XOP
crystal
X-ray server
WISE
COMSYL
Suite of Add-ons

## Slide 5: Source emission (XOPPY)
Undulator spectrum – power
Undulator power density
Wiggler spectrum
BM

## Slide 6
Computer simulation of light sources and optical components is a mandatory step in the design and optimization of synchrotron and FEL radiation beamlines
different codes for numerical simulations are available, implementing different physical approaches
RAY-TRACING
WAVEFRONT
PROPAGATION
Shadow
RAY
XRT
McXtrace
SRW
PHASE
WISE
WOFRY
COMSYL
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 7: At HIGH ENERGIES, WE ARE FAR FROM DIFFRACTION-LIMIT (=FULLY COHERENCE) U17 2m @ 17 keV (K=0.4842) L=2m Coherent Fraction THEREFORE, ANY BEAMLINE SIMULATION MUST START WITH RAY TRACING (INCOHERENT BEAMS)
3.13 %
0.18 %

## Slide 8: Oasys+ShadowOui
Install Oasys+ShadowOui:
  https://github.com/oasys-kit/oasys-installation-scripts/wiki
Today: Use rnice.
Download Tutorials:
  export all_proxy=http://proxy.esrf.fr:3128/
  git clone https://github.com/srio/ShadowOui-Tutorial
Start OASYS:
  oarsub –I –l nodes=1/cpu=1/core=8,walltime=10:00:00
  /scisoft/XRayOptics/OASYS1_RNICE8/start_oasys.sh

## Slide 9
Trace (the beamline)
p
y
z
x
q
z
x
x
y
z
Energy, Intensity

## Slide 10: Compute e- beam sizes
With e the emittance (constant), and Twiss parameters:
At waist (zero correlation, r=a=0, b is minimum):
At s (any point of the trajectory):
ShadowOui asks for s and e at waist (plus distance from waist to center of device)

## Slide 11: Onuki & Elleaume Undulators, Wigglers and their applications, CRC press, 2002
Undulator beams have not Gaussian profiles (even at resonances)
BY NOW, WE APPROXIMATE UNDULATORS BY GEOMETRIC SOURCES WITH GAUSSIAN SIZES AND DIVERGENCES
ex13_insertiondevices.ows

## Slide 12: Courtesy: Boaz Nash
(FOR UNDULATORS, THESE FORMULAS ARE VALID AT THE WAIST, AT THE UNDULATOR RESONANCE, AND SUPOSSING GAUSSIAN EMISSION OF PHOTONS)
ShadowOui performs “numeric convolution” by Monte Carlo sampling of the electron beam [Gaussian] and photon emission [non Gaussian]

## Slide 13: Optical elements
For each optics element SHADOW includes:
Geometrical model: how the direction of the rays are changed (reflected, refracted or diffracted)
Physical model: how the ray intensity (in fact electric fields) decreases because of the interaction
Structures along the surface =>playing with the direction
Structures in depth => playing with the reflectivity

## Slide 14: Mirrors Geometrical model Physical model
Fresnel equations give the reflectivity as a function of angle and photon energy. As a consequence, one gets the critical angle:
ex15_aberration.ows

## Slide 15: Mirror shape
q
p
r
r
Point to point focusing (ellipsoid)
Collimating (paraboloid)
Focalization in two planes
  Tangential or Meridional (ellipse or parabola)
  Sagittal (circle)
Demagnification: M=p/q
Easier manufactiring:
  2D: Ellipsoid => Toroid
  Only one plane: cylinder Ellipsoid (ellipse)=> cylinder (circle)
  Sagittal radius: non-linear (ellipsoid) => constant (cylinder) or linear (cone),
Aberrations
ex15_aberration.ows

## Slide 16: Kirkpatrick-Baez
ex16_kb.ows

## Slide 17: Crystals
BRAGG or reflection
LAUE or transmission
Geometrical model
like a grating originated by the truncation of the Bragg planes with the crystal surface. Crystals are dispersive elements, except for the most used case of Bragg-Symmetric reflection.
Physical model
(crystal reflectivity) is given by the Dynamical Theory of Diffraction and gives the “Darwin width”
(ex23_crystal_laue.ows)
ex17_sagittalfocusing.ows
OTHER_EXAMPLES/crystal_analyzer_diced.ows
OTHER_EXAMPLES/crystal_asymmetric_backscattering.ows

## Slide 18: Theory of the Use of More Than Two Successive X-Ray Crystal Reflections to Obtain Increased Resolving Power J W. M. DuMond Phys. Rev. 52, 872 – (1937) http://dx.doi.org/10.1103/PhysRev.52.872
ex17_crystalmono.ows

## Slide 19: Other
ex19_beamline.ows

## Slide 20: LENSE = TWO INTERFACES Geometrical model Physical model
CRL = n identical Lenses
TRANSFOCATOR = m different CRLs
absorption in media
  I/I0 = exp(-m t)
(OTHER_EXAMPLES/lens_elliptical.ows)
OTHER_EXAMPLES/CRL_Snigirev_1996.ows
ex24_transfocator.ows

## Slide 21: HYBRID METHOD IN SHADOW (X. Shi et al.) Combining ray tracing and wavefront propagation
Ray tracing of the beamline
Ideal lens with focal lengths of fx and fz